KDW- HP59AC12-80E/HP59AC20-80E/HP59AC30-80E

2.0Megapixel Full HD Network IR PTZ Dome Camera

Features

- 12X/20x/30x optical zoom

- Support dual-streams encoding

- Max. 25/30fps@1080P(1920 x1080) & 50/60fps@720P resolution

- DWDR, Day/Night(ICR), Ultra DNR, Auto iris, Auto focus

- Multiple network monitoring: Web viewer, CMS(DSS/PSS) & DMSS

- Max 400°/s pan speed, 360° endless pan rotation

- Up to 255 presets, 5 auto scan, 8 tour, 5 pattern

- Built-in 2/1 alarm in/out

- Support intelligent 3D positioning with DH-SD protocol

- Micro SD memory, IP66, POE+

- IR Distance up to 100m(AC24V)/80m(DC12V)

- Technical Specifications

| Model | KDW-HP59AC12-80E | KDW-HP59AC20-80E | KDW-HP59AC30-80E |
| --- | --- | --- | --- |
| Camera |
| Image Sensor | 1/2.8” 2.0Megapixel CMOS |
| Effective Pixels | 1944(H) x 1092(V) |
| Scanning System | Progressive |
| Electronic Shutter Speed | Auto/Manual,1/3~1/30000s |
| Min. Illumination | Color: 0. 05Lux/F1.6, B/W: 0.005Lux/F1.6 |
| S/N Ratio | >50dB |
| Camera Features |
| Day/Night | Auto(ICR) / Color / B/W |
| Backlight Compensation | BLC / HLC / DWDR(Digital WDR) |
| White Balance | Auto ,ATW, Indoor, Outdoor, Manual |
| Gain Control | Auto/Manual |
| Noise Reduction | Ultra DNR(2D/3D) |
| Privacy Masking | Up to 24 areas |
| Digital Zoom | 16x |
| Lens |
| Focal Length | 5.1mm ~61.2mm (12x Optical zoom) | 5.5mm ~110.0mm (20x Optical zoom) | 4.3mm ~129mm (30x Optical zoom) |
| Max Aperture | F1.6~F3.0 | F1.6~F3.5 | F1.6~F5.0 |
| Focus Control | Auto/Manual |
| Angle of View | H:51.3° ~ 4.64° | H:51° ~ 2.60° | H:65.1° ~ 2.34° |
| Close Focus Distance | 100mm ~ 1000mm |
| PTZ |
| Pan/Tile Range | Pan: 0° ~ 360° endless; Tilt: -15° ~ 90°, auto flip 180° |
| Manual Control Speed | Pan: 0.1° ~300°/s; Tilt: 0.1° ~200°/s |
| Preset Speed | Pan: 400°/s; Tilt: 300°/s |
| Preset | 300 |
| PTZ Mode | 5 Pattern, 8 Tour, Auto Pan, Auto Scan |
| Speed Setup | Human-oriented focal length/ speed adaptation |
| Power up Action | Auto restore to previous PTZ and lens status after power failure |
| Idle Motion | Activate Preset/Pan/Scan/Tour/Pattern if there is no command in the specified period |
| IR Distance | 80m(DV12V), 100m(AC24V) |
| Video |
| Video Compression | H.264/MJPEG |
| Resolution | 1080P(1920×1080)/720P(1280×720)/D1(704×576/704×480)/CIF(352×288/352×240) |
| Frame Rate | Main Stream | 1080P/720P(1 ~ 25/30fps)/720P(1~50/60fps) |
|  | Sub Stream | D1/CIF(1 ~ 25/30fps) |
| Bit Rate | H.264: 448K ~ 8192Kbps, MJPEG: 5120K~10240Kbps |
| Audio |
| Audio Compression | G.711a/G.711u(32kbps)/ PCM(128kbps) |
| Interface | 1/1 channel In/Out |
| Network |
| Ethernet | RJ-45 (10/100Base-T) |
| Network Protocol | Ipv4/Ipv6, HTTP, HTTPS, SSL, TCP/IP, UDP, UpnP, ICMP, IGMP, SNMP, RTSP, RTP, SMTP, NTP, DHCP, DNS, PPPOE, DDNS, FTP, IP Filter, QoS, Bonjour,802.1x |
| ONVIF | ONVIF PSIA CGI |
| Max. User Access | 20 users |
| Smart Phone | iPhone, iPad, Android, Windows Phone |
| Auxiliary Interface |
| Memory Slot | Micro SD, Max 64GB |
| Alarm | 2/1 channel In/Out |
| General |
| Power Supply | AC24V/DC12V+POE plus |
| Power Consumption | DC12V: 13W,20W(IR ON) AC24V: 13W,23W(IR ON) |
| Dimensions | Φ186(mm) x 309 (mm) |
| Weight | 3.5kg |
| Ingress Protection | IP66 |

Dimensions(mm)